## Slide 1
Contextual Bandit Hybrid Bit-Semantic Transmission Selection for UAVs
Likhita Sri Chakiri | [Member 2] | [Member 3]
Notes: PRESENTER: [Member 1]. Introduce the team and the title. One sentence: 'A UAV must decide, for every message, whether to send exact bits, the semantic meaning, or a compressed semantic version. We built a system that learns this decision online, sends real text messages through it, and evaluated it against baselines.'

## Slide 2
The problem: no single transmission mode is best
UAV-to-ground links swing between clear and blocked line-of-sight within seconds.
Battery and on-board compute are scarce, so wasted bits and wasted inference both cost.
Tasks differ: urgent alerts vs routine imagery; exact control commands vs images that tolerate approximation.
Static policies (always bit, always semantic) leave performance on the table.
Decision problem: 4 context signals, 3 actions, reward known only after acting, so it must be learned online.
Bit transmission
Exact, fast, but energy-hungry; fails hard in a poor channel.
Semantic transmission
Sends meaning only; degrades smoothly; needs neural inference (slower).
Compressed semantic
Lowest energy and most resilient at low SNR; lowest fidelity ceiling.
Machine Learning (25SC2107E) | Project Review 2
2
Notes: PRESENTER: [Member 1]. Explain the three modes and why none dominates: bit is exact but costly and brittle; semantic is lighter but slower and lossy; compressed semantic is cheapest and most resilient but least accurate. The decision depends on channel, urgency, delay budget and quality requirement, and the reward is only observed after acting, which is why a bandit is the natural formulation.

## Slide 3
Proposed method: a contextual bandit picks the mode
Context
SNR, urgency, delay budget, quality requirement (13 engineered features)
▶
Learner
LinUCB or Thompson Sampling (DQN as baseline)
▶
Action
bit, semantic or compressed semantic
▶
Reward
success minus urgency x latency minus energy
reward feedback after every task updates the learner
LinUCB
Per-mode ridge regression on the context
Chooses highest estimate plus uncertainty bonus
Explores where it is unsure (alpha = 1, tuned)
Thompson Sampling
Samples model weights from a Bayesian posterior
Acts greedily on the sampled model
Exploration comes from posterior spread (v = 0.6)
DQN (baseline)
Neural Q-network 64-64, replay buffer, target net
Can use battery and time-left as state
Plain NumPy; discount tuned (gamma = 0 in memoryless case)
reward = (+5 if quality ≥ requirement and latency ≤ deadline, else −3) − urgency weight × latency − 2 × energy
Machine Learning (25SC2107E) | Project Review 2
3
Notes: PRESENTER: [Member 1]. Walk left to right: the agent sees a context vector, picks one of three modes, gets a reward, and updates. LinUCB adds an uncertainty bonus to its estimate; Thompson Sampling samples from a posterior; both are contextual bandits. DQN is included as a baseline that can also use sequential state such as battery. Point out the reward formula: success is worth +5, failure costs 3, then subtract urgency-weighted latency and energy. The energy weight of 2 represents a battery-limited UAV; the sensitivity study later varies it from 0.5 to 4.

## Slide 4
How it works: from message to transmission
Message
text typed by the user
Analyzer
type, urgency, deadline, quality need
Context
features + channel SNR
Policy
trained LinUCB picks the mode
Send
bit, semantic or compressed
Receiver
quality, deadline, reward
Same message, four channel qualities: “Survey image shows flooded road near bridge,...”
Channel SNR | Mode chosen | Bytes sent | Quality | Outcome
0 dB | bit | 76 of 76 | 0.0 | failed (packet lost)
10 dB | bit | 76 of 76 | 1.0 | success
20 dB | semantic | 63 of 76 | 0.78 | success
28 dB | semantic | 63 of 76 | 0.78 | success
Weak channel: bit is still the best gamble, but it can be lost. Good channel: semantic saves bytes and energy at enough quality.
Try it yourself
python send_message.py \
"URGENT: obstacle ahead,
reduce altitude to 40 m" \
--snr 12 --compare
python send_message.py --interactive
python run_demo.py
Machine Learning (25SC2107E) | Project Review 2
4
Notes: PRESENTER: [Member 1]. This is the working system. (1) The user types a message. (2) The analyzer reads it: control commands need near-perfect quality, sensor readings moderate, image descriptions least; words like URGENT or 'within 2 seconds' set urgency and deadline; it also extracts key units (numbers, commands, entities). (3) Together with the channel SNR these become context features. (4) The trained LinUCB policy estimates the reward of each mode and picks the best. (5) The message is sent: bit sends the exact bytes (all-or-nothing); semantic sends only key units; compressed semantic sends the most important 80 percent dictionary-coded. (6) The receiver's quality is the fraction of key units that arrived; success needs quality and deadline; the reward is computed. The table shows one message at four channel qualities: at 0 dB bit is a gamble that lost the packet; at 10 dB bit works; at 20 and 28 dB the policy switches to semantic, sending 63 instead of 76 bytes and saving energy at quality 0.78, above the 0.65 needed for image reports. IMPORTANT to say: the semantic codec here is a transparent rule-based stand-in, not a trained neural codec, and the channel is the same simulated model the policy was trained on. Offer to run send_message.py live.

## Slide 5
Experimental setup
Simulator
Line-of-sight probability 0.6: SNR 15-30 dB, else -5 to 15 dB
3 task types x 3 urgency classes, each with deadline and quality requirement
Per-mode latency and energy; success needs quality and deadline
Energy weight 2 (battery-limited UAV)
Two settings
A: memoryless. 6,000 tasks per run, 10 seeds
B: battery-limited. 100 episodes x 200 tasks, battery budget 100 units, 5 seeds
Battery empty means transmission fails
Same information given to every learner
Compared
Baselines: always bit / semantic / compressed, random, threshold rule
Learners: epsilon-greedy, LinUCB, Thompson Sampling, DQN
Metrics: reward, regret vs oracle, success rate, latency, energy
Oracle = best expected mode per task (upper bound)
Machine Learning (25SC2107E) | Project Review 2
5
Notes: PRESENTER: [Member 2]. Be upfront that the simulator is synthetic: all numeric parameters are modelling assumptions we chose, not measurements. Explain why two settings: A tests the pure bandit formulation with independent tasks; B adds a battery budget so choices affect future options, which is where a sequential method like DQN could matter. Explain the oracle: for each task it picks the mode with the highest expected reward, so regret measures how much reward we lose by not knowing it. Hyper-parameters (alpha, v, epsilon, DQN learning rate and gamma) were chosen on three tuning seeds that are disjoint from the ten evaluation seeds. We also changed the default energy weight from 1 to 2 after noticing that at weight 1 the best fixed policy was already within 6% of the oracle; the sensitivity slide shows results from 0.5 to 4 so nothing is hidden.

## Slide 6
Result 1: learned policies beat all baselines
Chart: Average reward per task (10 seeds, 6,000 tasks)
| Oracle | LinUCB | Thompson Sampling | Epsilon-greedy | Always bit | DQN | Threshold rule | Random | Always compressed | Always semantic
Average reward per task | 0.696 | 0.507 | 0.503 | 0.442 | 0.423 | -0.082 | -0.822 | -2.095 | -3.219 | -3.534
Chart: Cumulative regret vs oracle (lower is better)
| 600 | 1200 | 1800 | 2400 | 3000 | 3600 | 4200 | 4800 | 5400 | 6000
Always bit | 163 | 328 | 498 | 669 | 830 | 998 | 1162 | 1320 | 1481 | 1642
Thompson Sampling | 173 | 298 | 429 | 555 | 687 | 811 | 937 | 1060 | 1181 | 1299
LinUCB | 155 | 276 | 396 | 513 | 633 | 752 | 869 | 979 | 1094 | 1206
DQN | 1534 | 2669 | 3470 | 3873 | 4010 | 4142 | 4271 | 4391 | 4516 | 4652
27%
less regret than always-bit, lower in 10 of 10 seeds (paired t = -3.83)
76.0%
task success (always-bit 76.5%) with 9% less energy
0.165
DQN regret per task after 20,000 tasks (LinUCB 0.185, always-bit 0.270)
Machine Learning (25SC2107E) | Project Review 2
6
Notes: PRESENTER: [Member 2]. Left: average reward: oracle 0.70, LinUCB 0.51, Thompson 0.50, always-bit 0.42. The hand-written threshold rule (-0.82) is WORSE than always-bit, which is an argument for learning; epsilon-greedy shows no significant gain (lower regret in 3 of 10 seeds). Right: regret is the reward lost versus the oracle, so flatter is better. LinUCB and Thompson flatten early; DQN loses a lot in its first thousand tasks. The gain is real but moderate: regret drops 27% (Thompson lower in 9/10 seeds, t = -2.80), success is unchanged, and the saving comes from spending less energy. The learners recover roughly 40 percent of the headroom between always-bit and the oracle. Bottom right: when we give DQN 20,000 tasks (3.3x more) its steady-state regret per task is 0.165 versus 0.185 for LinUCB and 0.270 for always-bit, so DQN needs about three times more data but then matches the bandits: its 0.02 lead over LinUCB is well inside LinUCB's seed-to-seed spread of about 0.06, so do not claim it is better. Its tuned discount is 0, meaning tuning found no benefit from looking ahead here.

## Slide 7
Result 2: what the policy learned
Chart: LinUCB mode choice by channel SNR (dB)
| -5–0 | 0–5 | 5–10 | 10–15 | 15–20 | 20–25 | 25–30
bit | 42 | 93 | 96 | 95 | 93 | 85 | 80
semantic | 5 | 3 | 2 | 0 | 0 | 0 | 0
compressed | 53 | 4 | 2 | 4 | 7 | 15 | 20
Chart: Context ablation (LinUCB reward)
| Full context | No urgency | No delay budget | No urgency AND no delay budget | No channel info | No quality requirement | Raw features only | No context
Average reward | 0.507 | 0.528 | 0.522 | 0.453 | 0.437 | 0.431 | 0.439 | 0.422
LinUCB picks the oracle's mode on 77% of tasks (always-bit: 65%). Channel, quality requirement and urgency/delay information each matter (removing any group costs 0.05-0.08 reward); without engineered margin features it falls back to always-bit. Urgency and delay budget only matter together (deadlines come from urgency): removing both gives 0.45.
Machine Learning (25SC2107E) | Project Review 2
7
Notes: PRESENTER: [Member 3]. Left chart: after learning, the policy shifts from bit at high SNR toward compressed semantic in weak channels, matching the oracle's pattern. It agrees with the oracle on 77% of tasks versus 65% for always choosing bit. Right chart: we removed one feature group at a time. Channel information and the quality requirement matter most, and urgency plus delay budget matter together. The 'no context' bandit converges to always-bit, and using only raw features (no engineered margin/slack features) also gives no gain, because success depends on threshold comparisons a linear model cannot form from raw inputs. Honest caveat: the engineered features use knowledge of the simulator's cost model, which a real deployment would have to estimate. Urgency and delay-budget features look useless individually because they are redundant (deadline is generated from urgency); removing both gives 0.45.

## Slide 8
Result 3: when does adaptation pay off?
Chart: Reward vs energy weight in the reward
| 0.5 | 1.0 | 2.0 | 3.0 | 4.0
Oracle | 1.929 | 1.489 | 0.688 | -0.086 | -0.833
LinUCB | 1.928 | 1.441 | 0.512 | -0.438 | -1.274
Always bit | 1.899 | 1.399 | 0.399 | -0.601 | -1.601
Chart: Battery-limited setting: reward after learning
| Always bit | Threshold | LinUCB | Thompson | DQN
Reward | -1.669 | -1.978 | -1.624 | -1.64 | -1.047
Energy scarcity drives the gain. Best-fixed-to-oracle gap grows from 0.03 to 0.77; LinUCB closes about 43% of it. With a battery budget, DQN wins: +0.62 over always-bit, best at every budget tested (60, 100, 140). Discount 0 scored best (-1.05 vs -1.22 at 0.9), so the edge appears to come from battery-aware nonlinear decisions rather than planning (not proven).
Machine Learning (25SC2107E) | Project Review 2
8
Notes: PRESENTER: [Member 3]. Left: when energy is cheap (weight 0.5) always-bit is almost optimal and adaptation adds little; as energy becomes scarce the oracle pulls away and the learners recover roughly 40 percent of the gap. Right: with a battery budget of 100 units per 200 tasks, every policy runs out of energy; the myopic bandits (even when given battery as a feature) barely beat always-bit, while DQN is clearly best, and it is best at budgets 60, 100 and 140. This partly contradicts our proposal, which expected DQN to be only marginally better: when energy is budgeted, sequential state matters. But when we tested discount factors, gamma = 0 was best, so we cannot claim that planning ahead is what helps; it looks like the network's use of battery state with nonlinear decisions. That is a hypothesis we have not fully isolated (we did not try engineered battery features for LinUCB). Limits: 100 episodes, 5 seeds.

## Slide 9
Conclusions and contributions
Delivered: project complete
✓ Simulator with deadlines, battery and channel model
✓ 5 baselines, 3 bandit learners, DQN
✓ Evaluation: comparison, ablation, sensitivity, battery, 20k-task DQN
✓ Working message system: send_message.py
✓ Reproducible repo: run_all.py, 9 tests, README, Colab notebook
Key findings
• Contextual bandits cut regret 27% vs always-bit; a hand rule made it worse
• Gain grows with energy scarcity (gap 0.03 to 0.77)
• With a battery budget DQN wins by +0.62
• On 16 real text messages: reward +0.83 vs +0.87 for always-bit, 12% less energy (on par, not better)
[Member 1]
Simulator (channel, tasks, costs, battery), baselines, message analyzer
[Member 2]
Features, LinUCB / Thompson / epsilon-greedy, tuning, ablation
[Member 3]
DQN, sensitivity and battery experiments, demo, README and GitHub
Machine Learning (25SC2107E) | Project Review 2
9
Notes: PRESENTER: all three members. State the outcome: the project is complete as scoped. Summarise the findings honestly: the gain over the best fixed policy is moderate (about 27 percent less regret, 40 percent of the available headroom); it grows when energy is scarce; with a battery budget DQN is best; and on our small set of 16 hand-written messages the learned policy is on par with always sending bits, not better, while using less energy. Limits to state proactively: the simulator is synthetic with assumed parameters; the semantic codec is a rule-based stand-in, not a trained neural codec; engineered features use knowledge of the cost model. Future work: a trained neural semantic codec and real channel traces. EACH MEMBER states their own contribution; EDIT THE THREE BOXES to reflect who actually did what before presenting.

## Slide 10
Thank you
Questions?
Likhita Sri Chakiri | [Member 2] | [Member 3]
Notes: PRESENTER: [Member 3] thanks the panel; all three answer questions. Offer to run send_message.py or run_demo.py live. Keep the Guide's Q&A section handy.